## Slide 1
Cameron Millard, Clean Energy Specialist
Environmental Sustainability
Town of Vail
Decarbonizing Snowmelt in Vail with Networked Geothermal
Matt Garlick CCP, CEM, BEMP
Managing Member
The GreyEdge Group

## Slide 2
Vail Climate Goals
Snowmelt and the Guest Experience
System Efficiency
Electrification Challenges
The Thermally Integrated Renewable Grid
The Decarbonization Journey
Vail Electric Snowmelt Boiler Heat Map
Notes: Also: Ease peak load demand
Turn liabilities into assets
Create new business models around energy
Shift paradigms about how energy is created, transferred, and shared

## Slide 3
Greening the Grid- The last 10%
Mountain Town Challenges
Building Electrification and EV Charging
The Falcon Curve
Grid Decarbonization

## Slide 4
Thermal Energy Networks (TEN)
Image Credit: HEET
Notes: ATL 101: Heat pumps to Heat Pump Buildings Heat Trading enabled. Can be connected to air, water, or ground.
Networked buildings (the TEN)
Move heat from lab to classroom, from civic buildings to residential
    (insert graphic)
    3 components
    Buildings
    Loop
    Thermal management devices

## Slide 5
Heat Pump Systems
Notes: System expansion and growth over time. Modularity of system is a huge benefit. Increased resiliency comes with expansion and diversity

## Slide 6
The ATL
Notes: Networked Buildings
Shared Loads and Assets
Liabilities can become Assets

## Slide 7
ATL Microgrids
Notes: System expansion and growth over time. Modularity of system is a huge benefit. Increased resiliency comes with expansion and diversity

## Slide 8
Hybrid Systems – the 50/90 Rule

## Slide 9
The Value of System Diversity

## Slide 10
Case Studies- Colorado Mesa University

## Slide 11
Case Studies- Colorado Mesa University
Without District System:
217 vertical feet of borehole per installed ton
Calculated water use: 14.5MM gallons/yr. (3,400 tons CT)
Electric Load 784 kW
With District System:
84 vertical feet of borehole per installed ton
Estimated Water Use: 4.5MM gallons (705 tons CT)
Electric Load: 185 kW
>$2,000,000 in annual utility savings

## Slide 12
Electric Demand Response
Notes: Thermal inertia is related to system size and mass
Ability to coast through peak events
CMU has 12 levels of demand response and
can hit button in response to XCEL Energy peak demand calls (Matt insert _______ here)

## Slide 13
The Vail Decarbonization Challenge
Climate Goals (50% by 2030)
Largest snowmelt in N. America?
Guest experience is important
System performance a must!
Peak load is late afternoon
Notes: (Vail snowmelt system map graphic)
Biggest snowmelt in north America (12 acres), 7megawatts of equivalent electrical energy (size of snowmelt plant
(insert pic)
Existing system serves town in many ways (slip and falls, snow storage and removal, cater to demographic that expects dry pavers (high-heel grade), risks for litigation
Covers Vail Village and Lionshead
Runs hot, was recently retro-commissioned (we are making more efficient)

## Slide 14
Energy and Carbon Reduction Potential in Vail
Notes: Vail is pursuing efficiency to reduce emissions, but to achieve goals we must reconsider the energy system type itself (equipment, fuel source, holistic opportunities). Benefit of efficiency is smaller alternative. Vail is pursuing both/and/all-of-the-above solutions.

## Slide 15
Thermal Energy Network Study- Phase 1
Initial Feasibility Study
50/90 decarbonization rule
Hydrogeology
Test Borehole
Thermal sources
Notes:   We conducted an advanced thermal conductivity test which involves pulsing heat into the ground and observing the rate of dissipation. This helps us understand the thermal battery potential of our geology (how quick to charge and discharge, and how long to store heat). (ability to transfer and store heat easily)
  Similar conditions throughout valley floor
  Evaluation of sources of thermal energy
ATL 101: Heat pumps to Heat Pump Buildings
  Heat Trading enabled
  Can be connected to air, water, or ground
  Networked buildings (the TEN)
    Move heat from lab to classroom, from civic buildings to residential
    (insert graphic)
    3 components
    Buildings
    Loop
    Thermal management devices

## Slide 16
Potential Thermal Management Assets in Vail
Notes: Partnership w/VR, ERWSD, Arrabelle has a 900 gpm dewatering system that could be a source of heat for the system. ERWSD treats up to 4million gallons daily and needs to reduce their temps under new state regulation. Creative solutions to heating involve taking advantage of existing waste heat opportunities (non-traditional waste-heat opportunities that can be capitizalized on with an TEN/ATL). (We will circle back to this on the paradigm shift slide). Are possible because of the nature of the TEN.

## Slide 17
Geothermal Energy Grant Program: Phase II Award
Colorado Energy Office – 7 million grant round.
Awarded TOV $250,000 for development of the Civic Area Geothermal Heating District, to include:
Wastewater treatment plant
Hotels like the Arrabelle
Library
Ice arena
Lionshead structure snowmelt plant
Geothermal Wells
Notes: Grant will eneable work: Beginning work on: MEP Design, Civic planning, risk Mitigation, IRA implications, Business model

## Slide 18
The Utility Thermal Energy Network (UTEN) Business Model
UTEN Conversation is Evolving Nationally
Who Finances, Owns, and Operates?
  Third Party
  Municipality or Customers
  Utility Company
Design, Commissioning and Controls Support
Billing and Customer Participation
Notes: Reliability of service
Cost-effectiveness (affordability for rate payers)
Falcon-curve (concept of smoothing out seasonal and daily demand patterns
Buffering variability
Sustainability and decarbonization
Opportunity to expand business (electric and gas service territories, this is the gold rush for clean, affordable, reliable heating and cooling)

## Slide 19
The Paradigm Shift
Beneficial Electrification is the challenge of our times- The last 10% is most difficult!
The TEN is a holistic tool to achieve decarbonization in the built environment
A TEN is a demand response tool that increases power factor of electrical grid
A TEN offers the highest possible COP for Heating and Cooling
In a TEN, Liabilities can become Assets
Notes: Reiterate problem (evolving demands on electric grid + need to decarbonize thermal loads) – i.e. beneficial electrification
Decarbonizing 90%, last 10% is most difficult
A TEN is a holistic tool to manage the challenge of electrifying thermal loads at scale w/high penetration of renewables in energy supply
It is an interactive grid for heating and cooling
From liabilities to assets
Smoothing out demand curve
Higher COP for heat pumps
  Higher efficiency
Stability
  Coasting through demand events w/thermal mass
Reiterate problem (evolving demands on electric grid + need to decarbonize thermal loads) – i.e. beneficial electrification
Decarbonizing 90%, last 10% is most difficult
A TEN is a holistic tool to manage the challenge of electrifying thermal loads at scale w/high penetration of renewables in energy supply
It is an interactive grid for heating and cooling
From liabilities to assets
Smoothing out demand curve
Higher COP for heat pumps
  Higher efficiency
Stability
  Coasting through demand events w/thermal mass
Reiterate problem (evolving demands on electric grid + need to decarbonize thermal loads) – i.e. beneficial electrification
Decarbonizing 90%, last 10% is most difficult
A TEN is a holistic tool to manage the challenge of electrifying thermal loads at scale w/high penetration of renewables in energy supply
It is an interactive grid for heating and cooling
From liabilities to assets
Smoothing out demand curve
Higher COP for heat pumps
  Higher efficiency
Stability
  Coasting through demand events w/thermal mass

## Slide 20
Thank you! Questions and Discussion
Cameron Millard
cmillard@vail.gov
Matthew Garlick
mgarlick@greyedgegroup.com